## Slide 1
PERFORMANCE / ENERGY STUDY
CPU x GPU Governor Study
DGX Spark
Latency, device time, power, and GPU EDP across the measured operating space
SOURCE governor_effects.csv
RAW RUNS
2,400
240 aggregate cells
WORKLOADS
30
GOVERNOR MODES
2 CPU / 4 GPU
01

## Slide 2
DECISION FRAME
One central question
DGX SPARK / CPU x GPU GOVERNORS
02
When does spending more power on frequency control produce a material, repeatable gain?
CPU governor
Host-side launch path
GPU governor
Device time + power
Workload
Bottleneck determines value
OUTPUT -> a transparent policy, not a universal max-performance setting

## Slide 3
2,400-RUN STUDY
Experimental design
DGX SPARK / CPU x GPU GOVERNORS
03
STUDY DESIGN
2,400 runs
full experiment
AGGREGATE CELLS
240
governor_effects.csv
WORKLOADS
30
observed labels
CPU
cpu_performance
cpu_powersave
GPU
gpu_default
gpu_ondemand
gpu_performance
gpu_powersave
WORKLOAD
babelstream-cuda
backprop-cuda
bfs-cuda
bh-cuda
cfd-cuda
fft-cuda
+ 24 more

## Slide 4
KEEP THE BOUNDARIES EXPLICIT
Metric definition
DGX SPARK / CPU x GPU GOVERNORS
04
GPU EDP
gpu_time² x GPU power
Device-side energy-delay proxy; lower is better
LAUNCH TIME
LATENCY ONLY
Never folded into GPU EDP
Why this matters
Avoids mixing host launch effects with device work
Makes CPU and GPU governor attribution interpretable
Preserves the measured units from source artifacts

## Slide 5
EVIDENCE HEALTH
Data quality and censoring
DGX SPARK / CPU x GPU GOVERNORS
05
AGGREGATE CELLS
240
CENSORED
60
GPU TIME VALID
234
EDP VALID
220
ARTIFACT-REPORTED FLAGS
Censoring and instrumentation

## Slide 6
THE GOVERNOR ONLY HELPS THE CONSTRAINED STAGE
Workload bottlenecks
DGX SPARK / CPU x GPU GOVERNORS
06
READOUT
CPU, GPU, memcpy, and launch timers may overlap and are nonadditive. The component plot is a bottleneck diagnostic, not a decomposition of launch latency.
CPU package power is absent on DGX Spark, so CPU EDP and whole-system EDP cannot be computed. CPU time and launch time are latency metrics only.
05_time_components_bottlenecks.png

## Slide 7
HOST-SIDE EFFECT
CPU governor impact on launch latency
DGX SPARK / CPU x GPU GOVERNORS
07
CPU PERFORMANCE
-2.8%
median application-latency change vs CPU powersave
CPU performance lowers latency in 106 of 117 comparable cells.
Largest application-level gains include babelstream, lavaMD, nw, pathfinder, and srad.
This is a host/application effect; GPU execution remains nearly unchanged.
02_cpu_impact_latency.png

## Slide 8
CROSS-DOMAIN COUPLING
CPU impact on GPU time and EDP
DGX SPARK / CPU x GPU GOVERNORS
08
GPU TIME
-0.0%
CPU performance vs CPU powersave; paired-cell median
GPU EDP
-0.2%
CPU performance vs CPU powersave; paired-cell median
INTERPRETATION
Treat host and device metrics independently
03_cpu_impact_gpu_edp.png

## Slide 9
TIME SAVED VERSUS POWER SPENT
GPU governor tradeoff
DGX SPARK / CPU x GPU GOVERNORS
09
ONDEMAND GPU EDP
+4.0% / +9.9%
CPU powersave / CPU performance; median vs default
POWERSAVE GPU EDP
+786% / +798%
~73% less power, but ~5x GPU time
Decision rule
Prefer lower EDP unless latency SLOs justify the power premium.
04_gpu_governor_edp_heatmaps.png

## Slide 10
WHERE POLICY EARNS ITS COMPLEXITY
Workload-specific wins
DGX SPARK / CPU x GPU GOVERNORS
10
BACKPROP / ONDEMAND
-51.5%
GPU EDP; <=2.2% latency; 10/10 repeats
LAVAMD / ONDEMAND
-2.5%
GPU EDP; no latency cost; 10/10 repeats
BH + NBODY
<1%
direction agrees, but practical significance is weak
06_valid_wins.png

## Slide 11
EVIDENCE FIRST; EXCEPTIONS EXPLICIT
Robust recommendations
DGX SPARK / CPU x GPU GOVERNORS
11
01
Use gpu_ondemand for backprop and lavaMD after a short guarded trial.
02
Treat bh and nbody as marginal candidates; their gains are below 1% and repeat consistency is weak.
03
Retain gpu_default for other measured workloads and for unknown applications.
04
Avoid gpu_powersave globally; only backprop shows a robust valid win. Never use it for censored gemmEx, mixbench, or myocyte cells.

## Slide 12
PORTABLE COUNTERS, INSPECTABLE DECISIONS
Transparent runtime policy
DGX SPARK / CPU x GPU GOVERNORS
12
01
Observe
launch latency / device time / utilization
02
Classify
host-bound / device-bound / insensitive
03
Select
lowest-cost governor meeting the SLO
04
Verify
re-sample; fall back on drift
PORTABLE SIGNAL CLASSES
SM active %
normalized SM clock
normalized memory clock
GPU power / temperature
launch latency sentinel

## Slide 13
WHAT MUST GENERALIZE BEFORE DEPLOYMENT
Limitations and x86 HPC next steps
DGX SPARK / CPU x GPU GOVERNORS
13
LIMITATIONS
CPU modes were measured on different dates; frequency is confounded with run-date and system drift.
CPU package power is unavailable, so CPU EDP and whole-system EDP are not reported.
Component timers may overlap and are diagnostic, not an additive launch-time decomposition.
Sub-percent EDP differences need reproduction before deployment.
X86 HPC VALIDATION
Repeat the full factorial design on target CPU and accelerator
Normalize counter classes, not platform-specific event names
Test NUMA, MPI rank placement, and multi-GPU contention
Validate policy under production power and thermal limits
Decision gate: reproduce direction, magnitude, and stability before rollout